## Slide 1: Exploiting Application Diversity in Throughput Processors
Xia Zhao

## Slide 2: Problems  Software  Hardware
Computing
platforms
Problems
Data storage
Scientific
Recognition
Software
Database system
Math libraries
Machine Learning

## Slide 3: Why GPUs?
Source: Hotchips19

## Slide 4: GPUs Are Changing the World

## Slide 5: Parallel Computing on GPUs
An array of N elements. Increment each element.
12
1
11
16
6
8
9
+1
13
2
12
17
7
9
10
CPU program
increment_cpu(float *a, float b, int N)
{
for (int idx = 0; idx<N; idx++)
a[idx] = a[idx] + 1;
}
GPU kernel
__global__ increment_gpu(float *a, float b, int N)
{
int idx = blockIdx.x * blockDim.x + threadIdx.x; if( idx < N) a[idx] = a[idx] + 1;
}
12
1
11
16
6
8
9
thrd
+1
thrd
+1
thrd
+1
thrd
+1
thrd
+1
thrd
+1
thrd
+1
12
1
11
16
6
8
9
thrd
+1
thrd
+1
thrd
+1
thrd
+1
thrd
+1
thrd
+1
thrd
+1
thrd
+1

## Slide 6: Hierarchical Programming Model
A GPU kernel is constructed of thread blocks
A thread block is constructed of threads
Block
(0,0)
Block
(1,0)
Block
(2,0)
Block
(0,1)
Block
(1,1)
Block
(2,1)
Block
(0,2)
Block
(1,2)
Block
(2,2)
GPU kernel

## Slide 7: GPU Hardware Architecture
Streaming Multiprocessor (SM)  computation resources
Last Level Cache (LLC) & memory  store data
Network-on-Chip (NoC)  comm. infrastructure
Network-on-Chip (NoC)
Memory
Controller
LLC
LLC
Memory
Controller
LLC
LLC
Memory
Controller
LLC
LLC
Memory
Controller
LLC
LLC
SM
SM
SM
SM
SM
SM
SM

## Slide 8: Map GPU Software to Hardware
Blocks within a GPU kernel are scheduled to SMs in a round-robin way
GPU cores within an SM execute the threads within a thread block
SM
SM
SM
Network-on-Chip (NoC)
Memory
Controller
LLC
LLC
Memory
Controller
LLC
LLC
Memory
Controller
LLC
LLC
Memory
Controller
LLC
LLC
SM
SM
SM
SM
Block
(0,0)
Block
(0,1)
Block
(0,2)
Block
(1,0)
Block
(1,1)
Block
(1,2)
Core
Core
Core
Core
Core
Core
Core
Core
Core
Core
Core
Core
Core
Core
SM

## Slide 9: A Wide Range of GPU Applications
Applications have different characteristics
 Application diversity
Source: NVIDIA

## Slide 10: Two Sources of Application Diversity
Applications have different data sharing degree
  Applications with no sharing
  Applications with moderate sharing
  Applications with high data sharing
Chart: Percentage of LLC Lines
| No sharing | Moderate sharing | High sharing
One SM | 1 | 0.77 | 0.33
Multiple SMs | 0 | 0.23 | 0.67

## Slide 11: Two Sources of Application Diversity
Applications have different data sharing degree
Different performance trend with SM count
  Compute-intensive application
  Memory-intensive application
Chart: Percentage of LLC Lines
| No sharing | Moderate sharing | High sharing
One SM | 1 | 0.77 | 0.33
Multiple SMs | 0 | 0.23 | 0.67
Chart: # of SMs
| 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 | 17 | 18 | 19 | 20 | 21 | 22 | 23 | 24
Compute-intensive | 0 | 0.040869 | 0.081553 | 0.12264 | 0.16312 | 0.20493 | 0.24622 | 0.28645 | 0.3286 | 0.37259 | 0.41164 | 0.45414 | 0.49577 | 0.53772 | 0.58019 | 0.6209 | 0.66541 | 0.70366 | 0.74988 | 0.79133 | 0.8318 | 0.87576 | 0.9209 | 0.9604 | 1
Memory-intensive | 0 | 0.2096 | 0.42915 | 0.62096 | 0.7663 | 0.87212 | 0.93057 | 0.9628 | 0.96907 | 0.97794 | 0.98296 | 0.98471 | 0.98411 | 0.98898 | 0.98897 | 0.99072 | 0.99636 | 0.99866 | 0.99535 | 0.99618 | 0.99435 | 0.99914 | 1 | 1 | 1

## Slide 12: Three Contributions of the Talk
SM
SM
SM
Network-on-Chip (NoC)
Memory
Controller
LLC
LLC
Memory
Controller
LLC
LLC
Memory
Controller
LLC
LLC
Memory
Controller
LLC
LLC
SM
SM
SM
SM
SM
SM
SM
SM
SM
SM
SM
SM
SM
SM
SM
1: Adaptive memory-side last-level caching [ISCA19]
2: SM partitioning in multitasking GPUs [ICS18]
3: Slowdown prediction for multitasking GPUs
[ASPLOS20]

## Slide 13: Three Contributions of the Talk
SM
SM
SM
Network-on-Chip (NoC)
Memory
Controller
LLC
LLC
Memory
Controller
LLC
LLC
Memory
Controller
LLC
LLC
Memory
Controller
LLC
LLC
SM
SM
SM
SM
SM
SM
SM
SM
SM
SM
SM
SM
SM
SM
SM
1: Adaptive memory-side last-level caching
2: SM partitioning in multitasking GPUs
3: Slowdown prediction for multitasking GPUs

## Slide 14: Shared LLC in Many-Core GPUs
GPUs adopt shared Last Level Cache (LLC) High cache capacity
Severe BW bottleneck for applications with concurrent accesses to shared data!!
SM
SM
Network-on-Chip (NoC)
Memory Controller
LLC
SM
SM
SM
SM
SM
SM
LLC
LLC
LLC
Problem: multiple SMs serialize on accesses to same shared cache line

## Slide 15: Sharing in Modern GPU Applications
Several modern GPU applications confirm the trend
Potential to improve performance by
eliminating BW bottleneck
More than 60% of data blocks are shared for such applications
Chart: Percentage of LLC Lines
| 类别 1
One SM | 0.3279
Multiple SMs | 0.6721

## Slide 16: How About Private LLC for GPUs?
SM
SM
Network-on-Chip (NoC)
Memory Controller
LLC
SM
SM
SM
SM
SM
SM
LLC
LLC
LLC
Shared data replicated across private LLC slices
Private vs shared LLC in GPUs: Capacity vs Bandwidth
 | Bandwidth (BW)
Shared | 1 line/cycle
Private | 4 lines/cycle
Higher bandwidth
Smaller capacity
SM
SM
Network-on-Chip (NoC)
Memory Controller
LLC
SM
SM
SM
SM
SM
SM
LLC
LLC
LLC

## Slide 17: GPU Application Demands
Three application categories
Shared-cache friendly: Capacity
Private-cache friendly: BW
Neutral applications
Chart: Normalized Performance
| Shared-cache friendly | Private-cache friendly | Neutral
Shared LLC | 1 | 1 | 1
Private LLC | 0.81923 | 1.3105 | 1.0019

## Slide 18: Adaptive Caching in GPUs
Dynamic technique to select best configuration at runtime
Online profiling to classify application’s LLC demand
Lightweight perf model to quantify BW vs hit rate benefits

## Slide 19: Adaptive Caching Mechanism
Shared LLC
Private LLC
Private miss rate is similar
Private BW > Shared BW
Periodically

## Slide 20: Miss Rate Prediction and Bandwidth Model
Estimating private LLC hit rate by using 
Set sampling based on auxiliary tag directory
Building bandwidth model based on 
LLC hit rate & LLC slice parallelism & memory bandwidth
Shared LLC
Private LLC
Private miss rate is similar
Private BW > Shared BW
Periodically
???
???

## Slide 21: Adaptive Memory-Side Last-Level Caching
Adaptive LLC Mechanism
Adaptive LLC and NoC Co-Design in GPUs
Experimental Results

## Slide 22: NoC-Enabled Adaptive LLC
Shared LLC configuration in GPUs
SM
SM
SM
Network-on-Chip
Memory
Controller
LLC
LLC
SM
SM
SM
SM
SM
SM
SM
SM
SM
SM
SM
SMs can access all LLC slices
LLC slice caches data from one MC (memory-side LLC)
LLC
Memory
Controller
LLC
LLC
LLC

## Slide 23: NoC-Enabled Adaptive LLC
Shared LLC configuration in GPUs
SM
SM
SM
2-Stage Hierarchical Xbar
Memory
Controller
LLC
LLC
SM
SM
SM
SM
SM
SM
SM
SM
SM
SM
SM
SMs can access all LLC slices
LLC slice caches data from one MC (memory-side LLC)
LLC
Memory
Controller
LLC
LLC
LLC
2-stage H-Xbar facilitates adaptive LLC policy

## Slide 24: Two-Stage Hierarchical Xbar (H-Xbar)
Two router stages: SM-side and MC-side routers

## Slide 25: Shared LLC Configuration with H-Xbar
In MC-Routers, full connectivity between inputs & outputs

## Slide 26: Shared LLC Configuration with H-Xbar
In MC-Routers, full connectivity between inputs & outputs
Each SM can reach each LLC slice

## Slide 27: Private LLC Configuration with H-Xbar
Simply bypass MC-router stage
Clusters of SMs have private LLC slice per MC
cluster
cluster
cluster

## Slide 28: Private LLC Configuration with H-Xbar
Simply bypass MC-router stage
Clusters of SMs have private LLC slice per MC
cluster
cluster
cluster

## Slide 29: Private LLC Configuration with H-Xbar
Simply bypass MC-router stage
Clusters of SMs have private LLC slice per MC
cluster
cluster
cluster

## Slide 30: Private LLC Configuration with H-Xbar
Simply bypass MC-router stage
Clusters of SMs have private LLC slice per MC
cluster
cluster
cluster

## Slide 31: NoC Power Optimization in Private LLC
MC-Routers are bypassed  power gate these routers
H-Xbar design enables power savings in private mode
cluster
cluster
cluster
Power-gated
Power-gated
Power-gated

## Slide 32: Adaptive Memory-Side Last-Level Caching
Adaptive LLC Mechanism
Adaptive LLC and NoC Co-Design in GPUs
Experimental Results

## Slide 33: Performance Improvement with Adaptive Caching
Chart: Normalized Performance
| Shared-cache friendly | Private-cache friendly | Neutral
Shared LLC | 1 | 1 | 1
Private LLC | 0.81923 | 1.3105 | 1.0019
Adaptive LLC | 1.0004 | 1.2806 | 1.0047
Improve perf. of private-friendly apps by avg 28.1%

## Slide 34: Performance Improvement with Adaptive Caching
Chart: Normalized Performance
| Shared-cache friendly | Private-cache friendly | Neutral
Shared LLC | 1 | 1 | 1
Private LLC | 0.81923 | 1.3105 | 1.0019
Adaptive LLC | 1.0004 | 1.2806 | 1.0047
Do not disturb performance of other applications

## Slide 35: Responsiveness Improvement with Adaptive Caching
High responsiveness leads to improved performance
Chart: LLC Response Rate
| Shared-cache friendly | Private-cache friendly | Neutral
Shared LLC | 4.2101 | 4.1065 | 2.2638
Private LLC | 3.4212 | 5.7293 | 2.3035
Adaptive LLC | 4.2108 | 5.6706 | 2.299

## Slide 36: NoC Energy Reduction with Adaptive Caching
Chart: Normalized NoC Energy
| Shared-cache friendly | Private-cache friendly | Neutral
Shared LLC | 1 | 1 | 1
Adaptive LLC | 1 | 0.7549 | 0.7156
24.5% NoC energy reduction for private-cache friendly

## Slide 37: NoC Energy Reduction with Adaptive Caching
Chart: Normalized NoC Energy
| Shared-cache friendly | Private-cache friendly | Neutral
Shared LLC | 1 | 1 | 1
Adaptive LLC | 1 | 0.7549 | 0.7156
28.4% NoC energy reduction for neutral applications

## Slide 38: Three Contributions of the Talk
SM
SM
SM
Network-on-Chip (NoC)
Memory
Controller
LLC
LLC
Memory
Controller
LLC
LLC
Memory
Controller
LLC
LLC
Memory
Controller
LLC
LLC
SM
SM
SM
SM
SM
SM
SM
SM
SM
SM
SM
SM
SM
SM
SM
1: Adaptive memory-side last-level caching
2: SM partitioning in multitasking GPUs
3: Slowdown prediction for multitasking GPUs

## Slide 39: Performance of Compute-Intensive Applications Increases Linearly
Chart: GPGPU-sim Results
| 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 | 17 | 18 | 19 | 20 | 21 | 22 | 23 | 24
DXTC | 0.040869 | 0.081553 | 0.12264 | 0.16312 | 0.20493 | 0.24622 | 0.28645 | 0.3286 | 0.37259 | 0.41164 | 0.45414 | 0.49577 | 0.53772 | 0.58019 | 0.62091 | 0.66541 | 0.70366 | 0.74988 | 0.79133 | 0.8318 | 0.87576 | 0.9209 | 0.9604 | 1
TPACF | 0.042427 | 0.084414 | 0.12613 | 0.16822 | 0.21015 | 0.25198 | 0.29375 | 0.33562 | 0.37752 | 0.41932 | 0.46106 | 0.50276 | 0.54435 | 0.58602 | 0.62768 | 0.66921 | 0.71082 | 0.75219 | 0.79357 | 0.83492 | 0.87635 | 0.9178 | 0.95897 | 1
BINO | 0.041929 | 0.083814 | 0.12575 | 0.16766 | 0.20956 | 0.25147 | 0.29339 | 0.33524 | 0.37726 | 0.41895 | 0.4612 | 0.50277 | 0.54478 | 0.5866 | 0.62869 | 0.66996 | 0.71157 | 0.75358 | 0.79517 | 0.83671 | 0.87806 | 0.91865 | 0.95929 | 1
LEU | 0.043191 | 0.086775 | 0.13064 | 0.17494 | 0.21883 | 0.26204 | 0.3047 | 0.34857 | 0.39058 | 0.43225 | 0.47508 | 0.51671 | 0.55661 | 0.59939 | 0.64153 | 0.68495 | 0.72413 | 0.76343 | 0.80395 | 0.84424 | 0.88428 | 0.92396 | 0.96206 | 1
CP | 0.04167 | 0.08328 | 0.1252 | 0.16684 | 0.20861 | 0.25004 | 0.29169 | 0.33363 | 0.37516 | 0.4164 | 0.45846 | 0.49993 | 0.54165 | 0.58351 | 0.62518 | 0.66663 | 0.70818 | 0.75004 | 0.79211 | 0.83361 | 0.87472 | 0.91696 | 0.95884 | 1
MERGE | 0.041873 | 0.083751 | 0.12565 | 0.16737 | 0.20924 | 0.25108 | 0.29295 | 0.33457 | 0.37661 | 0.4183 | 0.45985 | 0.50193 | 0.54362 | 0.58524 | 0.62685 | 0.66846 | 0.70983 | 0.75131 | 0.79289 | 0.83429 | 0.87551 | 0.91743 | 0.95828 | 1
PATHFINDER | 0.041995 | 0.083961 | 0.126 | 0.16798 | 0.21 | 0.25198 | 0.29396 | 0.33601 | 0.37806 | 0.42001 | 0.46199 | 0.5039 | 0.54143 | 0.58361 | 0.62505 | 0.66787 | 0.70785 | 0.75094 | 0.7931 | 0.83476 | 0.87446 | 0.91612 | 0.95924 | 1
Chart: P100 Results
| 1 | 4 | 8 | 12 | 16 | 20 | 24 | 28 | 32 | 36 | 40 | 44 | 48 | 52 | 56
DXTC | 0.018285 | 0.072949 | 0.14507 | 0.21855 | 0.29071 | 0.36278 | 0.43369 | 0.50759 | 0.57622 | 0.64741 | 0.72244 | 0.78883 | 0.85968 | 0.93059 | 1
TPACF | 0.021173 | 0.083412 | 0.16159 | 0.24249 | 0.31634 | 0.39045 | 0.45154 | 0.51685 | 0.57427 | 0.67758 | 0.6758 | 0.76407 | 0.77517 | 1.0025 | 1
BINO | 0.021029 | 0.079302 | 0.15804 | 0.2359 | 0.31298 | 0.38992 | 0.46655 | 0.54632 | 0.62409 | 0.67776 | 0.74433 | 0.84115 | 0.92185 | 1.0066 | 1
LEU | 0.019777 | 0.053549 | 0.11631 | 0.19946 | 0.29325 | 0.37069 | 0.45144 | 0.56186 | 0.63947 | 0.68066 | 0.74161 | 0.81235 | 0.86828 | 0.93666 | 1
CP | 0.018847 | 0.074249 | 0.14874 | 0.22371 | 0.29627 | 0.37125 | 0.4421 | 0.51644 | 0.58739 | 0.65948 | 0.73099 | 0.80032 | 0.87291 | 0.93918 | 1
MERGE | 0.018316 | 0.073083 | 0.14594 | 0.21891 | 0.29123 | 0.3636 | 0.43596 | 0.50383 | 0.58076 | 0.65445 | 0.71901 | 0.78648 | 0.85925 | 0.93285 | 1
PATHFINDER | 0.017951 | 0.071699 | 0.14336 | 0.21503 | 0.28654 | 0.35816 | 0.42962 | 0.50108 | 0.57251 | 0.64384 | 0.71509 | 0.78631 | 0.85683 | 0.92879 | 1

## Slide 40: Performance of Memory-Intensive Applications Saturates Quickly
Chart: P100 Results
| 1 | 4 | 8 | 12 | 16 | 20 | 24 | 28 | 32 | 36 | 40 | 44 | 48 | 52 | 56
LAVAMD | 0.085563 | 0.29764 | 0.52238 | 0.72617 | 0.88949 | 0.88773 | 0.93487 | 0.92483 | 0.95708 | 0.95913 | 0.95698 | 0.97535 | 0.99963 | 0.99991 | 1
GAUSSIAN | 0.054424 | 0.12617 | 0.25288 | 0.38427 | 0.50933 | 0.6383 | 0.76412 | 0.89296 | 1.0041 | 1.0516 | 0.97191 | 0.96401 | 0.96305 | 0.99338 | 1
LBM | 0.058471 | 0.20729 | 0.38715 | 0.54985 | 0.68937 | 0.81113 | 0.91002 | 0.95079 | 0.97283 | 0.98372 | 0.98517 | 0.99552 | 0.99471 | 0.99669 | 1
DWT2D | 0.044678 | 0.13489 | 0.25774 | 0.38005 | 0.49655 | 0.61761 | 0.75222 | 0.87345 | 0.9533 | 0.97622 | 0.98686 | 0.99304 | 0.99617 | 0.99805 | 1
GESUMMV | 0.08576 | 0.33167 | 0.64453 | 0.95331 | 1.2105 | 1.3696 | 1.3948 | 1.265 | 1.1404 | 1.0469 | 1.03 | 1.0172 | 0.9866 | 0.95921 | 1
PVC | 0.067644 | 0.24694 | 0.44588 | 0.58374 | 0.72911 | 0.80981 | 0.85348 | 0.89596 | 0.9229 | 0.94601 | 0.96073 | 0.97571 | 0.9895 | 0.99174 | 1
SC | 0.060823 | 0.19849 | 0.37153 | 0.53893 | 0.54014 | 0.9933 | 0.99238 | 0.99207 | 0.99579 | 0.99672 | 0.99377 | 0.99594 | 0.98388 | 0.99176 | 1
Chart: GPGPU-sim Results
| 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 | 17 | 18 | 19 | 20 | 21 | 22 | 23 | 24
LAVAMD | 0.1505 | 0.29902 | 0.44512 | 0.5843 | 0.7196 | 0.84801 | 0.94791 | 0.98762 | 0.95987 | 0.94994 | 0.94663 | 0.95347 | 0.9513 | 0.94861 | 0.94607 | 0.94271 | 0.95853 | 0.96591 | 0.96085 | 0.9648 | 0.9747 | 0.98708 | 0.99265 | 1
GAUSSIAN | 0.30352 | 0.59521 | 0.82405 | 0.9638 | 1.1414 | 1.2154 | 1.1968 | 1.1872 | 1.1653 | 1.1465 | 1.132 | 1.115 | 1.1001 | 1.0905 | 1.0753 | 1.0686 | 1.0589 | 1.0497 | 1.0375 | 1.0251 | 1.0157 | 1.0119 | 1.0075 | 1
LBM | 0.2096 | 0.42915 | 0.62096 | 0.7663 | 0.87212 | 0.93057 | 0.9628 | 0.96907 | 0.97794 | 0.98296 | 0.98471 | 0.98411 | 0.98898 | 0.98897 | 0.99072 | 0.99636 | 0.99866 | 0.99535 | 0.99618 | 0.99435 | 0.99914 | 1.0007 | 1.0016 | 1
DWT2D | 0.19459 | 0.38505 | 0.56766 | 0.71425 | 0.80291 | 0.86069 | 0.9052 | 0.93283 | 0.93861 | 0.94217 | 0.94834 | 0.95059 | 0.95579 | 0.96309 | 0.9671 | 0.97226 | 0.97659 | 0.97982 | 0.98447 | 0.98835 | 0.99167 | 0.99504 | 1 | 1
GESUMMV | 0.3274 | 0.65287 | 0.9578 | 1.1931 | 1.3458 | 1.4019 | 1.3696 | 1.353 | 1.3218 | 1.2359 | 1.2472 | 1.2098 | 1.1843 | 1.1907 | 1.1552 | 1.1412 | 1.1443 | 1.1312 | 1.0941 | 1.0579 | 1.021 | 1.0083 | 1.0034 | 1
PVC | 0.11489 | 0.22803 | 0.33878 | 0.44611 | 0.55068 | 0.65142 | 0.74549 | 0.82859 | 0.89398 | 0.93891 | 0.96412 | 0.97635 | 0.98316 | 0.98713 | 0.99021 | 0.99176 | 0.99448 | 0.99696 | 0.99856 | 1.0005 | 1.0008 | 1.0012 | 1.0007 | 1
SC | 0.13363 | 0.24118 | 0.36223 | 0.46313 | 0.57739 | 0.64611 | 0.72801 | 0.78436 | 0.82347 | 0.8446 | 0.87355 | 0.88239 | 0.88526 | 0.90337 | 0.892 | 0.90088 | 0.91189 | 0.92275 | 0.95094 | 0.95479 | 0.96719 | 0.97366 | 0.98311 | 1

## Slide 41: Resource Under-Utilization in Single Tasking
GPU
Compute-intensive
Application
GPU
Memory-intensive
Application
Memory resource
is under-utilized
Few memory accesses
Compute resource
is under-utilized
SMs are often stalled
due to memory accesses

## Slide 42: Multitasking Increases Resource Utilization
GPU
Compute-intensive
Application
Memory-intensive
Application
Memory & compute resources are well utilized

## Slide 43: Spatial Multitasking in GPUs
2 applications (App) execute on different SMs
Even SM partitioning  Each App has 10 SMs
  App1 – 10 SMs
  App2 – 10 SMs
GPU with 20 SMs
NoC&LLC&DRAM

## Slide 44: Alternative SM Partitioning
2 applications (App)
Even SM partitioning
  App1 – 10 SMs
  App2 – 10 SMs
Uneven SM partitioning
GPU with 20 SMs
NoC&LLC&DRAM

## Slide 45: Alternative SM Partitioning
2 applications (App)
Even SM partitioning
  App1 – 10 SMs
  App2 – 10 SMs
Uneven SM partitioning
Power-gating some SMs
GPU with 20 SMs
NoC&LLC&DRAM
Compute & Memory applications have different requirements
How to find the most effective SM partition?
Power
gated

## Slide 46: SM Partitioning in Multitasking GPUs
SM partitioning in GPU multitasking
Classification-driven search
Experimental results

## Slide 47: Performance Optimization Opportunities for Heterogeneous Workloads
Heterogeneous workload
A memory-intensive app
A compute-intensive app
Chart: System Performance
| 12 | 11 | 10 | 9 | 8 | 7 | 6 | 5 | 4 | 3 | 2 | 1
LBM_DXTC | 1.3636 | 1.4055 | 1.4532 | 1.5002 | 1.549 | 1.5916 | 1.6224 | 1.6175 | 1.5779 | 1.4884 | 1.354 | 1.1776
NoC&LLC&DRAM
# of SMs assigned to the memory-intensive application
Key message  Opportunities to increase performance
Insight  Move SMs from memory app to compute app

## Slide 48: Power Optimization Opportunities for Homogeneous Workloads
Homogeneous workload
Memory-intensive app1
Memory-intensive app2
Chart: System Performance
| 24 | 22 | 20 | 18 | 16 | 14 | 12 | 10 | 8 | 6 | 4 | 2
LBM_DWT2D | 1.0058 | 1.0037 | 1.0005 | 1.0004 | 0.99608 | 0.99156 | 0.99175 | 0.99766 | 0.99802 | 0.95565 | 0.7711 | 0.41837
# of SMs assigned to the
co-executing apps
NoC&LLC&DRAM
Key message  Opportunities to save power
Insight  Allocate less SMs to memory-intensive app

## Slide 49: Classification-Driven Search
Workloads executing
on GPUs
Classification model
Heterogeneous workloads
Homogeneous workloads
Performance mode
Power
mode
Effective SM partition to improve performance
Effective SM partition to save power

## Slide 50: Classification-Driven Search
Workloads executing
on GPUs
Classification model
Heterogeneous workloads
Homogeneous workloads
Performance mode
Power
mode
Effective SM partition to improve performance
Effective SM partition to save power

## Slide 51: Classification Model
Bandwidth demand: how much SMs need
  A model based on MPKI and IPC per SM
Bandwidth supply: how much GPUs provide
  A model based on NoC, LLC and memory bandwidth
Bandwidth demand > Bandwidth supply  memory-bound application
Bandwidth demand < Bandwidth supply  compute-bound application

## Slide 52: Classification-Driven Search
Workloads executing
on GPUs
Classification model
Heterogeneous workloads
Homogeneous workloads
Performance mode
Power
mode
Effective SM partition to improve performance
Effective SM partition to save power

## Slide 53: Performance Mode
Start with even SM partitioning, record perf.
Iteratively stall the SMs assigned to the mem-app
Stop stalling when perf. of mem-app changes
Assign stalled SMs to compute-app
GPU with 20 SMs
NoC&LLC&DRAM

## Slide 54: Classification-Driven Search
Workloads executing
on GPUs
Classification model
Heterogeneous workloads
Homogeneous workloads
Performance mode
Power
mode
Effective SM partition to improve performance
Effective SM partition to save power

## Slide 55: Power Mode
Start with even SM partitioning, record perf.
Stall all but leave only one SM for each mem-app
GPU with 20 SMs
NoC&LLC&DRAM

## Slide 56: Power Mode
Start with even SM partitioning, record perf.
Stall all but leave only one SM for each mem-app
Estimate the SM count based on IPC estimation
Iteratively resume one SM until saturation
GPU with 20 SMs
NoC&LLC&DRAM
Power-
Gated

## Slide 57: SM Partitioning in Multitasking GPUs
Motivation
Classification-driven search
Experimental results

## Slide 58: CD-Search Improves Performance
STP (system throughput). Higher-is-better
ANTT (average normalized turnaround time). Lower-is-better
Chart: Sorted heterogeneous workloads
STP | -0.021185 | -0.020732 | -0.020656 | -0.019528 | -0.005434 | -0.004981 | -0.003669 | 0.001187 | 0.010935 | 0.014222 | 0.034205 | 0.039271 | 0.040442 | 0.046455 | 0.051474 | 0.065892 | 0.12438 | 0.13365 | 0.13452 | 0.13588 | 0.13588 | 0.1491 | 0.14982 | 0.15351 | 0.1574 | 0.15902 | 0.15982 | 0.16146 | 0.1663 | 0.16973 | 0.1698 | 0.17142 | 0.17848 | 0.18637 | 0.18681 | 0.19267 | 0.2307 | 0.23121 | 0.24151 | 0.24743 | 0.25145 | 0.32133 | 0.32771 | 0.35304 | 0.36205 | 0.37117 | 0.42298 | 0.45864 | 0.62853
ANTT | -1.9891 | -1.2697 | -1.0483 | -1.0328 | -0.78083 | -0.65091 | -0.62178 | -0.55404 | -0.55206 | -0.53629 | -0.51905 | -0.47544 | -0.43817 | -0.41766 | -0.38236 | -0.38233 | -0.32434 | -0.32207 | -0.32038 | -0.29762 | -0.2958 | -0.28738 | -0.28092 | -0.28015 | -0.27977 | -0.27733 | -0.27393 | -0.27088 | -0.26608 | -0.26256 | -0.25363 | -0.25202 | -0.22456 | -0.14919 | -0.14638 | -0.11417 | -0.11384 | -0.11187 | -0.10725 | -0.10197 | -0.006648 | -0.002796 | 0.002619 | 0.003493 | 0.006104 | 0.006722 | 0.010032 | 0.010726 | 0.010842
10.4% STP improvement
22% ANTT improvement

## Slide 59: CD-Search Decreases Power Consumption
Chart: Sorted homogeneous workloads
Power | -0.41129 | -0.39296 | -0.37302 | -0.35489 | -0.29943 | -0.29752 | -0.28792 | -0.28588 | -0.25718 | -0.24743 | -0.24275 | -0.23556 | -0.2225 | -0.2212 | -0.22061 | -0.21209 | -0.18873 | -0.10526 | -0.03467 | -0.015126 | -0.009797
25% power reduction

## Slide 60: Three Contributions of the Talk
SM
SM
SM
Network-on-Chip (NoC)
Memory
Controller
LLC
LLC
Memory
Controller
LLC
LLC
Memory
Controller
LLC
LLC
Memory
Controller
LLC
LLC
SM
SM
SM
SM
SM
SM
SM
SM
SM
SM
SM
SM
SM
SM
SM
1: Adaptive memory-side last-level caching
2: SM partitioning in multitasking GPUs
3: Slowdown prediction for multitasking GPUs

## Slide 61: Resource Contention in Multitasking GPUs
App1 is executing alone
 Single tasking
App1 is co-executing with App2
 Multitasking
NoC & LLC & DRAM
NoC & LLC & DRAM
No Resource Contention

## Slide 62
App1 is executing alone
 Single tasking
App1 is co-executing with App2
 Multitasking
Resource Contention
>
Resource Contention in Multitasking GPUs
NoC & LLC & DRAM
NoC & LLC & DRAM
No Resource Contention
Per-application performance degrades because of resource contention under multitasking:

## Slide 63: Cloud Providers Require Fairness and QoS Support in Multitasking GPUs
Fairness support
  Goal: Co-executing applications experience similar slowdown
Quality of Service (QoS) support
  Goal: Pre-set and meet a per-application performance target
Predicting slowdown plays a critical role in fairness and QoS support

## Slide 64: Slowdown Prediction in Multitasking GPUs
is obtained through online profiling
is unknown during multitasking
Unknown
Known
How to predict application slowdown?

## Slide 65: Slowdown Prediction in Multitasking GPUs
Motivation
Hybrid Slowdown Model (HSM)
Experimental results

## Slide 66: White-box Model vs Black-box Model
White-box model [1]
Use architectural insights
Low hardware cost
Hard to capture overlap effects
Black-box model [2]
Use ML to learn features
High hardware cost
Can capture overlap effects
pipeline
stall
cache
miss
branch
prediction
row conflict
White-box model
Black-box model
[1] Hu et al. Run-Time Performance Estimation and Fairness-Oriented Scheduling Policy for Concurrent GPGPU Applications, ICPP2016. [2] Zhao et al. Themis: Predicting and Reining in Application-Level Slowdown on Spatial Multitasking GPUs, IPDPS2019.

## Slide 67: Hybrid Slowdown Model (HSM) Benefits From Both Worlds
Lessons from white-box model
Using architectural insights to reduce cost
Lessons from black-box model
Using ML to model non-trivial overlaps
 | White-box | Black-box | HSM
Overlap modeling | ✗ | ✓ | 
Cost | ✓ | ✗ | 
✓
✓

## Slide 68: Hybrid Slowdown Model (HSM)
Overview
Slowdown
prediction
Compute-bound
Slowdown
prediction
Memory-bound
Kernel
Classifier

## Slide 69: Hybrid Slowdown Model (HSM)
Overview
Slowdown
prediction
Compute-bound
Slowdown
prediction
Memory-bound
Kernel
Classifier
????

## Slide 70: Performance of Compute-Bound Kernels Increases Linearly with SM Count
Chart: # SM
| 2 | 10 | 20 | 30 | 40 | 50 | 60 | 70 | 80
DXTC | 0.024991 | 0.050028 | 0.074972 | 0.099942 | 0.12508 | 0.14994 | 0.17495 | 0.19996 | 0.22496 | 0.24997 | 0.27497 | 0.29993 | 0.3249 | 0.35034 | 0.37529 | 0.40041 | 0.42548 | 0.45041 | 0.47554 | 0.50059 | 0.52555 | 0.55058 | 0.57561 | 0.60065 | 0.62567 | 0.65055 | 0.67585 | 0.70079 | 0.72578 | 0.75077 | 0.77594 | 0.80091 | 0.82596 | 0.85093 | 0.87595 | 0.90108 | 0.92599 | 0.95107 | 0.97602 | 1
HOTSPOT | 0.025073 | 0.050132 | 0.075265 | 0.10036 | 0.12538 | 0.15009 | 0.17551 | 0.20016 | 0.22586 | 0.25023 | 0.27589 | 0.30114 | 0.32625 | 0.35109 | 0.37614 | 0.40027 | 0.42667 | 0.45145 | 0.47528 | 0.50026 | 0.52652 | 0.55027 | 0.57517 | 0.60017 | 0.6252 | 0.65021 | 0.67523 | 0.70201 | 0.727 | 0.75024 | 0.77514 | 0.80011 | 0.82521 | 0.85011 | 0.87519 | 0.90014 | 0.92521 | 0.95009 | 0.97532 | 1
PF | 0.025033 | 0.050096 | 0.075157 | 0.1002 | 0.12524 | 0.15022 | 0.17528 | 0.2004 | 0.22546 | 0.25049 | 0.27541 | 0.30056 | 0.32542 | 0.35045 | 0.37546 | 0.40053 | 0.42549 | 0.45054 | 0.47572 | 0.50049 | 0.52549 | 0.55091 | 0.57632 | 0.60089 | 0.62623 | 0.65076 | 0.67594 | 0.70136 | 0.72641 | 0.75139 | 0.7762 | 0.80101 | 0.82607 | 0.8502 | 0.87557 | 0.90049 | 0.92551 | 0.95016 | 0.97474 | 1
BINO | 0.026187 | 0.052567 | 0.078882 | 0.10516 | 0.13145 | 0.15775 | 0.18404 | 0.21036 | 0.23669 | 0.26287 | 0.28918 | 0.31551 | 0.34174 | 0.36807 | 0.3944 | 0.42023 | 0.4444 | 0.46909 | 0.49493 | 0.51928 | 0.54201 | 0.56791 | 0.59214 | 0.61779 | 0.64175 | 0.66533 | 0.68984 | 0.71314 | 0.73485 | 0.7579 | 0.77988 | 0.80299 | 0.83359 | 0.85842 | 0.88112 | 0.90786 | 0.93147 | 0.9524 | 0.9786 | 1
MRI-Q | 0.025553 | 0.051045 | 0.076575 | 0.102 | 0.1276 | 0.15306 | 0.17858 | 0.2038 | 0.22945 | 0.25483 | 0.2797 | 0.30545 | 0.32978 | 0.35531 | 0.38016 | 0.40686 | 0.43027 | 0.45574 | 0.48051 | 0.50633 | 0.52957 | 0.55572 | 0.5792 | 0.60622 | 0.6289 | 0.65389 | 0.67845 | 0.7045 | 0.72896 | 0.75403 | 0.77871 | 0.80388 | 0.82684 | 0.85474 | 0.87443 | 0.90795 | 0.92615 | 0.94762 | 0.97604 | 1
SM count can be used to predict application slowdown

## Slide 71: Slowdown Prediction Based on SM Count
SM count under multitasking, which is obtained during execution
SM count under single tasking, i.e., all SMs in the GPU

## Slide 72: Hybrid Slowdown Model (HSM)
Overview
Slowdown
prediction
Compute-bound
Slowdown
prediction
Memory-bound
Kernel
Classifier
????

## Slide 73: Performance of Memory-Bound Kernels Correlates with Memory Bandwidth Utilization
Chart: #SM
| 2 | 10 | 20 | 30 | 40 | 50 | 60 | 70 | 80
PVC | 0.3514 | 0.67639 | 0.85791 | 0.92849 | 0.97153 | 0.99434 | 1.0109 | 1.0217 | 1.0281 | 1.0333 | 1.0375 | 1.0395 | 1.042 | 1.043 | 1.0436 | 1.044 | 1.0447 | 1.0439 | 1.0433 | 1.0416 | 1.0411 | 1.0407 | 1.0409 | 1.0381 | 1.0368 | 1.0366 | 1.0321 | 1.0317 | 1.0289 | 1.0257 | 1.0249 | 1.0187 | 1.0206 | 1.0174 | 1.0143 | 1.0122 | 1.0097 | 1.009 | 1.0075 | 1
LBM | 0.40279 | 0.7845 | 0.91377 | 0.9381 | 0.96132 | 0.96911 | 0.97036 | 0.96024 | 0.94686 | 0.92906 | 0.92437 | 0.9257 | 0.92431 | 0.92676 | 0.93454 | 0.93347 | 0.93972 | 0.94409 | 0.95186 | 0.95001 | 0.95528 | 0.96261 | 0.96372 | 0.96142 | 0.97634 | 0.97431 | 0.97573 | 0.97511 | 0.98107 | 0.98107 | 0.98935 | 0.97686 | 0.99089 | 0.99015 | 0.98754 | 0.99058 | 0.99588 | 0.99684 | 0.99887 | 1
BH | 0.11322 | 0.22648 | 0.33971 | 0.45287 | 0.56623 | 0.67869 | 0.75312 | 0.77082 | 0.79995 | 0.8254 | 0.85283 | 0.87461 | 0.90069 | 0.91763 | 0.92215 | 0.91996 | 0.94779 | 0.95444 | 0.95974 | 0.96642 | 0.97476 | 0.97791 | 0.98148 | 0.97421 | 0.98416 | 0.98156 | 0.98172 | 0.98021 | 0.98288 | 0.98634 | 0.9861 | 0.98971 | 0.98756 | 0.98921 | 0.99015 | 0.99661 | 0.99469 | 0.99804 | 1.011 | 1
DWT2D | 0.13705 | 0.25621 | 0.34636 | 0.41884 | 0.4812 | 0.53319 | 0.59049 | 0.65408 | 0.75921 | 0.81874 | 0.85605 | 0.89581 | 0.92088 | 0.94513 | 0.96557 | 0.98374 | 0.99389 | 0.99947 | 0.99945 | 0.99851 | 0.99942 | 0.99952 | 1.0009 | 1.0001 | 0.99991 | 1.0001 | 0.99946 | 0.9999 | 1.0003 | 0.9992 | 1.0005 | 1.0003 | 1.0002 | 1.0007 | 1.0005 | 0.99991 | 1.0005 | 1.0004 | 1 | 1
EULER3D | 0.2295 | 0.36122 | 0.44986 | 0.54341 | 0.88595 | 0.95773 | 0.95858 | 0.96596 | 0.97265 | 0.98118 | 0.9848 | 0.99332 | 0.9939 | 0.99497 | 0.99558 | 0.99598 | 0.9959 | 0.99585 | 0.99699 | 0.99649 | 0.99846 | 0.99699 | 0.99766 | 0.99751 | 0.99789 | 0.99717 | 0.99664 | 0.99685 | 0.9976 | 0.99759 | 0.99737 | 0.99942 | 0.99722 | 0.99851 | 0.99864 | 0.999 | 0.99876 | 0.9988 | 0.99973 | 1
FWT | 0.14105 | 0.27164 | 0.40663 | 0.51561 | 0.60799 | 0.68366 | 0.75323 | 0.81289 | 0.87151 | 0.91861 | 0.96641 | 1.0004 | 1.0074 | 1.0006 | 1.0028 | 1.0019 | 1.0018 | 1.001 | 1.0009 | 1.0042 | 1.0027 | 1.0012 | 1.0008 | 1.0035 | 1.0011 | 1.0005 | 0.99993 | 1.0028 | 1.0003 | 1.0025 | 0.99879 | 1.0015 | 0.99906 | 0.9981 | 0.99844 | 1.0015 | 0.99678 | 1.0014 | 0.99825 | 1
2DCONV | 0.044066 | 0.086692 | 0.12926 | 0.17227 | 0.21492 | 0.25789 | 0.2984 | 0.33847 | 0.3772 | 0.41298 | 0.44738 | 0.47822 | 0.51272 | 0.54546 | 0.57311 | 0.59173 | 0.63266 | 0.66252 | 0.69032 | 0.71891 | 0.74635 | 0.77346 | 0.79517 | 0.82105 | 0.8429 | 0.86314 | 0.88256 | 0.90193 | 0.91806 | 0.93423 | 0.94613 | 0.95803 | 0.96841 | 0.97567 | 0.98185 | 0.98708 | 0.99036 | 0.99338 | 0.99821 | 1
SC | 0.11005 | 0.2187 | 0.32583 | 0.42436 | 0.50631 | 0.57229 | 0.62115 | 0.65738 | 0.69056 | 0.72421 | 0.74729 | 0.77588 | 0.77042 | 0.77104 | 0.79629 | 0.80722 | 0.83192 | 0.86693 | 0.89346 | 0.88471 | 0.91945 | 0.91909 | 0.95818 | 0.93622 | 0.95393 | 0.95275 | 0.95325 | 0.93208 | 0.9631 | 0.9658 | 0.95983 | 0.97098 | 0.96232 | 0.94957 | 0.96566 | 0.99324 | 0.97932 | 0.99042 | 0.98254 | 1
CONVS | 0.037286 | 0.074553 | 0.11183 | 0.14904 | 0.18638 | 0.22364 | 0.26091 | 0.29789 | 0.33538 | 0.37251 | 0.40955 | 0.44646 | 0.48335 | 0.51925 | 0.5552 | 0.59231 | 0.62826 | 0.66385 | 0.69997 | 0.73357 | 0.76988 | 0.8038 | 0.83762 | 0.86432 | 0.88715 | 0.9096 | 0.92679 | 0.93948 | 0.94738 | 0.95598 | 0.95826 | 0.96954 | 0.97481 | 0.97856 | 0.98455 | 0.9845 | 0.98113 | 0.99205 | 0.98781 | 1
SRAD | 0.077804 | 0.1544 | 0.23061 | 0.30014 | 0.35971 | 0.41138 | 0.45342 | 0.49651 | 0.53294 | 0.56458 | 0.60404 | 0.62526 | 0.64977 | 0.67263 | 0.69004 | 0.71136 | 0.72345 | 0.76378 | 0.78874 | 0.80988 | 0.85468 | 0.84726 | 0.91389 | 0.95136 | 0.9225 | 0.97582 | 0.98949 | 0.99134 | 0.99375 | 0.99591 | 0.99357 | 0.99497 | 0.99807 | 0.99705 | 1.0028 | 1.0016 | 1.0038 | 1.0019 | 1.0035 | 1
Memory bandwidth utilization
can be used to predict application slowdown
Chart: #SM
| 2 | 10 | 20 | 30 | 40 | 50 | 60 | 70 | 80
PVC | 0.34195 | 0.6693 | 0.85178 | 0.92248 | 0.96532 | 0.98829 | 1.0035 | 1.0137 | 1.0198 | 1.0254 | 1.0288 | 1.0301 | 1.0317 | 1.0326 | 1.0326 | 1.0321 | 1.0329 | 1.0319 | 1.0306 | 1.0294 | 1.0283 | 1.0268 | 1.0262 | 1.024 | 1.0225 | 1.0214 | 1.0185 | 1.0176 | 1.0158 | 1.0136 | 1.013 | 1.0085 | 1.0099 | 1.0073 | 1.0062 | 1.0048 | 1.0038 | 1.004 | 1.003 | 1
LBM | 0.3549 | 0.68863 | 0.80934 | 0.8325 | 0.8542 | 0.86252 | 0.86935 | 0.87933 | 0.89245 | 0.89995 | 0.91101 | 0.91718 | 0.92017 | 0.92596 | 0.93463 | 0.93343 | 0.94159 | 0.94488 | 0.95298 | 0.95217 | 0.95802 | 0.96427 | 0.9673 | 0.96426 | 0.97912 | 0.97582 | 0.98035 | 0.9782 | 0.98487 | 0.98434 | 0.99262 | 0.97852 | 0.99429 | 0.99304 | 0.98983 | 0.9926 | 0.99773 | 0.99835 | 1 | 1
BH | 0.11445 | 0.22897 | 0.34338 | 0.45719 | 0.57063 | 0.68311 | 0.75775 | 0.77521 | 0.80389 | 0.83007 | 0.85681 | 0.87879 | 0.90503 | 0.9219 | 0.92638 | 0.92387 | 0.95199 | 0.95819 | 0.96332 | 0.9699 | 0.97834 | 0.98101 | 0.98479 | 0.97665 | 0.98684 | 0.98386 | 0.98422 | 0.9821 | 0.98469 | 0.98795 | 0.98754 | 0.9913 | 0.98854 | 0.9898 | 0.99114 | 0.99679 | 0.99472 | 0.99794 | 1.0111 | 1
DWT2D | 0.13786 | 0.2577 | 0.34835 | 0.42122 | 0.48395 | 0.53608 | 0.59382 | 0.65757 | 0.76314 | 0.82215 | 0.86029 | 0.89985 | 0.92494 | 0.95025 | 0.96984 | 0.98745 | 0.99773 | 1.0037 | 1.0034 | 1.0021 | 1.0027 | 1.0025 | 1.0037 | 1.0026 | 1.0025 | 1.0026 | 1.0017 | 1.0017 | 1.0017 | 1.0011 | 1.0014 | 1.0017 | 1.0015 | 1.0012 | 1.001 | 1.0004 | 1.0011 | 1.0006 | 0.99996 | 1
EULER3D | 0.23096 | 0.36332 | 0.4526 | 0.5461 | 0.89032 | 0.96225 | 0.96271 | 0.96984 | 0.97647 | 0.9843 | 0.98881 | 0.99654 | 0.99767 | 0.99836 | 0.99881 | 0.99927 | 0.99858 | 0.99794 | 0.99971 | 0.99908 | 1.0002 | 0.99973 | 0.99978 | 0.99932 | 0.99983 | 0.99959 | 0.99815 | 0.99802 | 0.99862 | 0.99832 | 0.99781 | 1.0003 | 0.99815 | 0.99887 | 0.99889 | 0.99928 | 0.99925 | 0.99883 | 0.99999 | 1
FWT | 0.1263 | 0.25934 | 0.39675 | 0.50765 | 0.60177 | 0.67878 | 0.74973 | 0.8105 | 0.87026 | 0.91811 | 0.9668 | 1.0013 | 1.0086 | 1.0016 | 1.0035 | 1.0024 | 1.0023 | 1.0016 | 1.0015 | 1.0047 | 1.0031 | 1.0018 | 1.0017 | 1.0041 | 1.0013 | 1.0011 | 1.0003 | 1.0029 | 1.0001 | 1.0029 | 0.99908 | 1.0016 | 0.9997 | 0.99834 | 0.99851 | 1.0012 | 0.99722 | 1.0014 | 0.99795 | 1
2DCONV | 0.044389 | 0.087061 | 0.12968 | 0.17272 | 0.21543 | 0.25845 | 0.29901 | 0.33911 | 0.37788 | 0.4137 | 0.44811 | 0.47894 | 0.51352 | 0.54622 | 0.574 | 0.59256 | 0.63349 | 0.66341 | 0.69122 | 0.71979 | 0.74726 | 0.77437 | 0.79606 | 0.82192 | 0.8438 | 0.864 | 0.88333 | 0.90278 | 0.91891 | 0.93498 | 0.9469 | 0.95881 | 0.96921 | 0.9764 | 0.98238 | 0.98768 | 0.99087 | 0.99352 | 0.99827 | 1
SC | 0.10728 | 0.21437 | 0.31818 | 0.41477 | 0.49692 | 0.55176 | 0.60252 | 0.64237 | 0.67632 | 0.69958 | 0.71477 | 0.74515 | 0.74571 | 0.75184 | 0.77714 | 0.78618 | 0.80285 | 0.82638 | 0.84174 | 0.83042 | 0.86286 | 0.86552 | 0.90217 | 0.88718 | 0.90516 | 0.90921 | 0.91213 | 0.89815 | 0.92936 | 0.9354 | 0.93127 | 0.94853 | 0.95218 | 0.94797 | 0.95794 | 0.98352 | 0.9799 | 0.99393 | 0.98633 | 1
CONVS | 0.027853 | 0.06369 | 0.09969 | 0.13567 | 0.17187 | 0.20786 | 0.24403 | 0.27963 | 0.31562 | 0.35126 | 0.38673 | 0.42231 | 0.45771 | 0.49228 | 0.52758 | 0.56322 | 0.59912 | 0.63439 | 0.6703 | 0.70399 | 0.74025 | 0.77441 | 0.80966 | 0.83549 | 0.86001 | 0.88728 | 0.90505 | 0.92284 | 0.93343 | 0.9435 | 0.94736 | 0.96033 | 0.96764 | 0.97172 | 0.97902 | 0.98124 | 0.97668 | 0.9877 | 0.98692 | 1
SRAD | 0.064088 | 0.14365 | 0.2216 | 0.29534 | 0.35708 | 0.41087 | 0.45263 | 0.50001 | 0.53202 | 0.56552 | 0.60694 | 0.62496 | 0.64848 | 0.67535 | 0.6957 | 0.70785 | 0.72804 | 0.76534 | 0.7878 | 0.81004 | 0.85153 | 0.84856 | 0.91343 | 0.95411 | 0.91458 | 0.97941 | 0.99344 | 0.99497 | 0.99781 | 0.99959 | 0.99617 | 0.99806 | 0.99961 | 0.9997 | 1.0034 | 1.0012 | 1.0034 | 1.0021 | 1.0034 | 1

## Slide 74: Slowdown Prediction Based on Memory Bandwidth Utilization
Bandwidth utilization under multitasking is obtained during execution
Bandwidth utilization under single tasking (unknown)

## Slide 75: Row Buffer Hit Rate (RBH) Determines Memory Bandwidth Utilization
Bank-level parallelism is maximized in GPUs
RBH determines idle time of banks in DRAM
Chart: Row buffer hit rate (RBH)
| 1.9E-2 | 0.19678699999999999 | 0.28952899999999998 | 0.72139600000000004 | 0.425705 | 0.59712299999999996 | 0.93656300000000003 | 0.23319000000000001 | 0.74795900000000004 | 0.60387500000000005
 | 0.35869 | 0.44428 | 0.48999 | 0.71619 | 0.5705 | 0.66749 | 0.76358 | 0.47846 | 0.68013 | 0.62387
Bank 1
Bank 2
Bank n
Row X
Row Y
Row Y
Access Row Y: Hit
Access Row Y: Hit
Access Row X: Miss
Row
Buffer
Organization of an HBM channel

## Slide 76: Row Buffer Hit Rate is Similar under Single Tasking as Multitasking
Reason: FR-FCFS prioritizes row-hit requests from the same application
Chart: Row buffer hit rate
| PVG | LBM | BH | DWT2D | EULER3D | FWT | 2DCONV | SC | CONVS | SRAD | AVG
Single tasking | 0.019991 | 0.19679 | 0.28953 | 0.7214 | 0.42571 | 0.59712 | 0.93656 | 0.23319 | 0.74796 | 0.60388 | 0.47721
Multitasking | 0.032441 | 0.14545 | 0.21066 | 0.59112 | 0.37693 | 0.5172 | 0.7645 | 0.15422 | 0.71664 | 0.57775 | 0.40869

## Slide 77: Slowdown Prediction Based on Memory Bandwidth Utilization
and are obtained through offline profiling
is obtained during the execution

## Slide 78: Hybrid Slowdown Model (HSM)
Overview
Slowdown
prediction
Compute-bound
Slowdown
prediction
Memory-bound
Kernel
Classifier
????

## Slide 79: Compute- versus Memory-Bound Classifier
Bandwidth demand
Executed instructions
Memory accesses
Operating frequency
Bandwidth utilization potential
Theoretical bandwidth (e.g., 900GB/s)
Row buffer hit rate
Bandwidth demand > Bandwidth utilization  memory-bound kernel
Bandwidth demand < Bandwidth utilization  compute-bound kernel
Total hardware cost of the model and the classifier equals 0.8 KB

## Slide 80: HSM-based SM Allocation Policies
Divide execution time into epochs (500K cycles)
Reallocate SMs at the end of each epoch
Time (clock cycles)
SM1
SM2
SM3
SM4
SM5
App 1
App 2
App 1
App 2
Predict slowdown
HSM-fair  fairness target
HSM-QoS  QoS target
Epoch n
Epoch n+1

## Slide 81: Slowdown Prediction in Multitasking GPUs
Motivation
Hybrid Slowdown Model (HSM)
Experimental Results

## Slide 82: Experimental Setup
Performance evaluation
GPGPU-sim  GPU
Ramulator  HBM
Volta-like GPU configuration
80 SMs with 48KB L1
4 HBM stacks: 900GB/s
8 channels per HBM stack
6MB LLC
15 applications
Rodinia
CUDA SDK
Parboil
PolyBench
Mars

## Slide 83: High Accuracy of HSM
Chart: 
| HSM | DASE | Themis
 | 0.068083 | 0.17948 | 0.33793
6.8% prediction error on average
[1] Hu et al. Run-Time Performance Estimation and Fairness-Oriented Scheduling Policy for Concurrent GPGPU Applications, ICPP2016. [2] Zhao et al. Themis: Predicting and Reining in Application-Level Slowdown on Spatial Multitasking GPUs, IPDPS2019.
Chart: Sorted all workloads

## Slide 84: Fairness-Aware SM Allocation
Chart: Sorted all workloads
HSM-Fair achieves 84.1% fairness

## Slide 85: QoS-Aware SM Allocation
Chart: Sorted all workloads
HSM-QoS meets the QoS target for all workloads
QoS target = 0.8 normalized progress
Notes: HSM-QoS

## Slide 86: Comparing against Memory Bandwidth Partitioning
Chart: Sorted all workloads
Chart: Sorted all workloads
HSM-Fair outperforms previous approaches
based on bandwidth partitioning
[1] Jog et al. Anatomy of GPU Memory System for Multi-Application Execution, MEMSYS2015.

## Slide 87: Three Contributions of the Talk
SM
SM
SM
Network-on-Chip (NoC)
Memory
Controller
LLC
LLC
Memory
Controller
LLC
LLC
Memory
Controller
LLC
LLC
Memory
Controller
LLC
LLC
SM
SM
SM
SM
SM
SM
SM
SM
SM
SM
SM
SM
SM
SM
SM
1: Adaptive memory-side last-level caching [ISCA19]
2: SM partitioning in multitasking GPUs [ICS18]
3: Slowdown prediction for multitasking GPUs
[ASPLOS20]

## Slide 88: Thank You
Exploiting Application Diversity in Throughput Processors
Xia Zhao